## Slide 1: A Review and Analysis of Eye-Gaze Estimation
Paper Summary

## Slide 2: Paper Structure
Gaze Tracking Fundamentals
Gaze Estimation Algorithms
User Platforms Implementing Gaze Tracking
Performance Metrics and Platform-Specific Error Sources
Performance Evaluation Framework

## Slide 3: Gaze Tracking Fundamentals
Fixations: Eyes stationary. Visual input
Saccades: Rapid, involuntary. Between Fixations
Scan-Path: Fixations + Saccades until eye reaches target
Gaze Duration
Pupil Size

## Slide 4: Typical Eye Model
Visual Axis
  Fovea to corneal curvature
  Defines gaze
  Cannot be measured 
Optical Axis
  Pupil center to corneal curvature
  Can be measured
Kappa Angle
  Unique
  Can be obtained through calibration
  Optical Axis + Kappa = Visual Axis 

## Slide 5: Active Estimation Methods
Use NIR LED Induced Glint
2D Regression Based:
  Done by mapping Pupil Center  Corneal Glint vector
Cross Ratio Based:
  Rectangular pattern projection for head pose estimation
3D Model Based*:
  Use a geometrical eye model to estimate center of cornea, optical and visual axis
Notes: *There is a 3D model based method using a Kinect, which makes that method passive
PCCR – Pupil Center Corneal Reflection

## Slide 6: Passive Estimation Methods - Appearance Based
Use shape and texture
  Eye contour
  Iris size, location
  Positions of pupils
Estimation through best fit
Low HW req.

## Slide 7: Passive Estimation Methods - Shape Based
Fits parabolas, circle to eye contour, iris
Vulnerable to:
  Head movement
  Eye occlusion

## Slide 8: Passive Estimation Methods – 3D Model Based
Three works use a depth camera (Kinect)
Kinect used to obtain head pose, iris and eyeball centers
Calibration used to obtain 3D coordinates of eye parameters
Allows head movement
Notes: Depth:
[62] -K. Wang and Q. Ji, ``Real time eye gaze tracking with Kinect”
[63]- X. Zhou, H. Cai, Z. Shao, H. Yu, and H. Liu, ``3D eye model-based
gaze estimation from a depth sensor”
[64] - L. Jianfeng and L. Shigang, ``Eye-model-based gaze estimation by
RGB-D camera”

## Slide 9: Algorithms Summary – Pros & Cons
Method | Pros | Cons
2D Regression | Utilizes Features of human eye Easy to implement | Not robust to movements
3D Model | Robust to movements | Hard and Expensive implementation
Cross Ratio | Do Not rely on 3D Do not require Calibration Robust to movements | Very dependent of user distance and environmental factors
Appearance Based | Relatively Cheap implementation | Not accurate as PCCR methods Requires large DB of tagged data (For NN training) Not robust to movements or illumination
Shape Based | Relatively Cheap implementation Sufficient accuracy | Not robust to movements or occlusions High computational complexity (Similarity calculations) Model initialization issues

## Slide 10: User Platforms Implementing Gaze Tracking
The paper presents 5 main user platforms:
  Desktop Based
  TV and Large Display Panels
  Head-Mounted Setups (VR, AR, etc.)
  Automotive
  Hand-Held (Smartphones, Tablets, etc.)
Unique conditions, accuracy and best algorithm
Typical Accuracy:
  Head-Mounted – less than 1 degree
  Desktop – 0.5-2 degrees
  Automotive and Hand-Held (Dynamic Platforms) - >2 degrees
The same tracker may supply different results for different platforms
Notes: Table – Different user poses and conditions in different platforms

## Slide 11: Performance Metrics and Platform-Specific Error Sources
Works in gaze estimation evaluate their results in any of:
  Angular resolution [deg.]
  Gaze recognition rate [%]
  Shift from ground truth [pix.] , [cm.]
Operating conditions rarely taken into consideration or characterized
Therefore most gaze estimation methods cannot be inter compared
Currently - no comprehensive practice for performance evaluation

## Slide 12: Suggested Performance Evaluation Framework
To understand the effects of different factors, a methodology composed of the following experiments, with a set of realistic test values, is proposed
  Head pose impact (roll, pitch & yaw)
  Various illumination (color temperature and intensities)
  User distance and viewing angle
  Display size and resolution
  Occlusions (e.g. glasses)
  Platform movement
Work still in progress

## Slide 13: What’s next?
Given an RGB-D camera, which method would be the best?
What are the Realsense’ capabilities? Can it be used to estimate the user’s different characteristics (cornea curvature, head pose)?
Should we consider/use the suggested Performance Evaluation Framework?
If 3D Model method is the way, on which model should we focus? Do we have enough data?
How can a NN classify to almost continuous output?